## Slide 1: Efficient Wideband Spectrum Sensing Using MEMS Acoustic Resonators
Junfeng Guan, Jitian Zhang, Ruochen Lu, Hyungjoo Seo,
Jin Zhou, Songbin Gong, Haitham Hassanieh

## Slide 2
Changes in the Wireless Spectrum
Released 1.2 GHz unlicensed spectrum in 6 GHz (Wi-Fi 6E)
April 2020
October 2020
Expanded unlicensed wireless operations in TV White Spaces
Authorized full commercial deployment in 3.5 GHz CBRS band
January 2020
Citizens Broadband Radio Service (CBRS) band
Tier 1: Incumbent Access
Tier 2: Priority Access License
Tier 3: General Authorized Access

## Slide 3: Improve Spectrum Use Efficient Through Sharing
Citizens Broadband Radio Service (CBRS) band
Tier 1: Incumbent Access
Tier 2: Priority Access License
Tier 3: General Authorized Access
Sharing
Exploit previously underutilized spectrum
Accommodate new wireless services
Dynamic spectrum sharing scheme
Conventional per-band
Spectrum access paradigm
CBRS band
TV White Spaces
Wi-Fi 6E

## Slide 4: Enabling Dynamic Spectrum Sharing
Requirement for unlicensed devices:
Find and access momentarily idle channels
Sense wideband (100s of MHz to GHz) spectrum in real-time
Sampling at the Nyquist sampling rate
High-speed
ADC
Expensive
High power consumption
Real-time wideband spectrum sensing is
challenging for mobile and IoT devices

## Slide 5: Existing Spectrum Sensing Technologies
Frequency Sweeping
Sequential scanning
- monitoring each narrow band for a short period time.
Cannot continuously sense all bands in real-time.
Easily miss highly dynamic and fleeting signals such as radar waveforms.
Compressive Sensing or Sparse Fourier Transform Algorithms
Only work when the spectrum is sparsely occupied.
Defeat the purpose of efficiently utilizing the spectrum.

## Slide 6
New Spectrum Sensing Strategy
Vacant Channel
Finding a vacant wireless channel as
finding an open spot in a parking lot.

## Slide 7
New Spectrum Sensing Strategy

## Slide 8: S3 – Spectrum Sensing Spike-Train
Sparse Frequency Sampled Spectrum
Densely Occupied Wideband Spectrum
Detected Spectrum Occupancy
Features of S3:
Real-time occupancy
Wideband
8.5x below Nyquist sampling → Low power consumption
Densely occupied spectrum
Sampling along the frequency axis
Monitor sampled
fraction of bandwidth

## Slide 9: S3 – Spectrum Sensing Spike-Train
Sparse Frequency Sampled Spectrum
Densely Occupied Wideband Spectrum
Detected Spectrum Occupancy
Features of S3:
Real-time occupancy
Wideband
8.5x below Nyquist sampling → Low power consumption
Densely occupied spectrum
Sampling along the frequency axis
Monitor sampled
fraction of bandwidth
How can we sample a spectrum along the frequency axis?

## Slide 10: Enabled of Frequency Sampling
Sparse Frequency Sampled Spectrum
Densely Occupied Wideband Spectrum
Frequency Response
Microscope Image
Spike-Train Filter
Narrow, sharp, and periodic passbands
Sample the signal below the Nyquist sampling rate
and still be recover the channel occupancies.

## Slide 11: Spike-Train Filter Created by MEMS Acoustic Resonators
Piezoelectric Thin Film
Electrodes
Width W
RF to Acoustic
Acoustic to RF
Input
Output
MEMS: Micro-Electro-Mechanical Systems
Resonance frequencies
determined by geometry of the piezoelectric material.

## Slide 12: Spike-Train Filter Created by MEMS Acoustic Resonators
19 spikes
22MHz spacing
418MHz bandwidth

## Slide 13: Recover Spectrum Occupancy
Aliasing
Detected Spectrum Occupancy
Digitized Spectrum
with Ambiguity & Collisions
Sub-Nyquist Sampling
Low-Speed
ADC
S3 Recovery Algorithm
Leveraging
Structured Sparsity
Sub-Nyquist Sampling
at a different rate
Resolving
Ambiguity & Collisions
Low-Speed
ADC
Sparse Frequency
Sampled Spectrum
S3
Recovery Algorithm
Sub-Nyquist
Sampling
Challenge 1:
Reconstructing wideband spectrum occupancy
from sub-Nyquist sampled time-domain signals.
Detected Spectrum Occupancy
Sampling below the Nyquist rate results in Aliasing

## Slide 14: Co-prime sub-sampling factor avoids frequency collisions
1
2
3
4
5
7
8
9
10
6
Spike-Train
11
0
1
2
3
4
5
0
Sub-sample by factor of 2
Collision
Frequency
Avoid Frequency Collisions
Sub-sample by factor of 3
(co-prime with
number of spikes K)
0
1
2
3
1
2
3
4
5
7
8
9
10
6
11
0
Frequency
Structured Sparsity Pattern
Co-prime sub-sampling factor guarantees no collisions

## Slide 15: S3 with Non-Ideal Spike-Train Filter
Sampling rate = 52.74 MHz
Sampling rate = 45.5 MHz
(MHz)
Frequency Response
(Normalized)
Challenge 2: Non-ideal spike-train filter in practice.
Frequency Collision
Not in Collision
Different sampling rates exhibit frequency collisions between different spikes

## Slide 16
TX USRPs
TX USRPs
TX USRPs
S3 Receiver
2.2m
2m
2.1m
Evaluation Using Spectrum Sensing Testbed

## Slide 17
Occupancy Detection Accuracy
False Positive Rate: Percentage of empty bands that S3 incorrectly reports as occupied.
False Negative Rate: Percentage of occupied bands that S3 incorrectly reports as empty.
 | 10% | 50% | 90%
BigBand | 0.38%+14% (unresolved) | N/A | N/A
D-BigBand | 0.95% | 1.75% | 3%
SweepSense | 4.88% | 13.09% | 13.76%
S3 | 0.00% | 1.29% | 2.47%
 | 10% | 50% | 90%
BigBand | 0.38%+14% (unresolved) | N/A | N/A
D-BigBand |  |  | 
SweepSense | 4.88% | 13.09% | 13.76%
S3 | 0.00% | 1.29% | 2.47%
Comparison Against State-of-the-Art Prior Work

## Slide 18
Spectrum Analyzer Ground Truth
GHz
(a)
(b)
(d)
Power Spectral Density
Spike Occupancy
Extend S3 to Capture Power Spectral Density
Testbed 1.8~2.4 GHz
Outdoor 1.8~2.4 GHz
Indoor 5.4~6 GHz
Indoor 2.1~2.7 GHz
Combining frequency sampling and sweeping
Power Spectrum Density Captured by S3

## Slide 19
S3 – Spectrum Sensing Spike-Train:
Efficient real-time wideband spectrum sensing mechanism.
Can work in densely occupied spectrum.
Leverages RF MEMS filtering solution to enable sampling the spectrum along the frequency axis.
Can be extended to capture power spectral density.
Conclusion
For more details, please check out our paper:
https://www.usenix.org/conference/nsdi21/presentation/guan